## Slide 1: Technical exchange: Ireland’s PaMs reporting
October 2025

## Slide 2: Overview
Summary of data from 2025 reporting cycle
Approach and workflow
The national system for PaMs and Projections

## Slide 3
Summary of data from 2025 reporting cycle

## Slide 4: Number of PaMs reported
Chart: 
| Total PaMs | PaMs under both WEM and WAM | PaMs under WEM or WAM only
WEM | 45 | 28 | 17
WAM | 46 | 28 | 18
91
56
35

## Slide 5: GHG emission reductions
Note: graph excludes LULUCF PaMs
Achieved
Expected
Chart: kt CO2 eq
| 2023 | 2025 | 2030 | 2035 | 2040 | 2045 | 2050
Reductions from implemented PaMs | 14968.1046 | 17901.4441 | 27142.4921 | 36235.8217 | 42357.4749 | 45730.0246 | 50649.0875
Additional reductions from planned PaMs | 0 | 859.5766 | 5960.7348 | 6491.3734 | 7089.3963 | 7620.6686 | 8032.2656

## Slide 6: Alignment: PaMs and Projections
Source: EEA Technical report No 4/2015

## Slide 7: Alignment: PaMs and Projections
Chart: Kt CO2 eq
| 2025 | 2030 | 2035 | 2040 | 2045 | 2050 | 2055
Filler | 53749.3053 | 46084.6851 | 42456.2873 | 39005.9745 | 36356.7911 | 33766.186 | 33013.7978
WAM PaMs effect | 859.5766 | 5960.7348 | 6491.3734 | 7089.3963 | 7620.6686 | 8032.2656 | 8469.9506
WEM PaMs effect | 17901.4441 | 27142.4921 | 36235.8217 | 42357.4749 | 45730.0246 | 50649.0875 | 52883.2848
WEM projections | 54608.8818 | 52045.4199 | 48947.6607 | 46095.3707 | 43977.4597 | 41798.4517 | 41483.7484
WAM projections | 53565.4361 | 45035.9373 | 41361.3612 | 37880.6058 | 34733.061 | 31701.6233 | 30333.8313
Note: graph excludes LULUCF emissions and LULUCF PaMs

## Slide 8
Approach and workflow

## Slide 9: Approach - PaMs
Quantitative assessment of PaMs is underpinned by the same set of projected activity data and underlying scenario assumptions as those used to produce the national GHG projections
Three streams of data compilation:
Initiatives and supports typically delivered through SEAI
e.g. Electric Vehicle Deployment
Energy Efficiency PaMs
Measures that go beyond energy efficiency including the use of renewables
Other Energy PaMs
Measures related to Agriculture and LULUCF and the smaller IPPU and Waste sectors
Non-Energy PaMs

## Slide 10: Three streams of data compilation
Chart: Number of PaMs
| Total | Energy efficiency PaMs | Other energy PaMs | Non-energy PaMs
WEM | 45 | 36 | 4 | 5
WAM | 46 | 26 | 4 | 16
Number of PaMs by data stream and projections scenario
91
62
21
8

## Slide 11
SEAI energy savings
EPA Emission Factors
PaMs Tool
Data Processing
[MS Excel]
Annex (PaMs attributes and progress)
Extract, Transform, Load
(Mostly manual)
Load
Annex XIV
(Air Quality)
Integrated national policies and measures – GovReg
Transform
(Manual)
Other energy and non-energy PaMs
[e.g. Ag, LULUCF, Renewables]

## Slide 12: PaMs tool
In 2015, EPA commissioned Aether to create a PaMs tool for calculation and collation of energy PaMs
  Tool updated in 2019 to generate savings from Ireland's energy PaMs for reporting under the Monitoring Mechanism Regulation
GHG and air pollutant emissions savings calculated based on data from SEAI
  Energy savings (TWh/year) for each PaM, by fuel group
  Fuel splits for each PaM, as percentage across solid fossil fuel, oil, gas, electricity, renewables
  Sectors allocated to each PaM from industry, residential, services and transport
  Emission factors applied to energy savings specific to sector, fuel and year

## Slide 13: PaMs tool
The PaMs tool is based in an Excel workbook
  uses the data manipulation functionalities of a relational database (Microsoft Access) to generate GHG and air quality emissions savings
The tool includes two components:
    Excel workbook
      to manage input data and gather output data
      linked to the Access database and includes the output data through links to the database using Excel pivot tables
    Access database
      functions in the background to complete the data table joining and combining tasks
      performs queries on the input data taken from the Excel workbook, the results of which are included in the Excel workbook
      the Access database does not need to be open to update results

## Slide 14
SEAI energy savings
EPA Emission Factors
PaMs Tool
Data Processing
[MS Excel]
Annex (PaMs attributes and progress)
Extract, Transform, Load
(Mostly manual)
Load
Annex XIV
(Air Quality)
Integrated national policies and measures – GovReg
Transform
(Manual)
Other energy and non-energy PaMs
[e.g. Ag, LULUCF, Renewables]

## Slide 15: Other energy PaMs
Impacts of these PaMs calculated through counterfactuals and assumptions around fossil fuel displacement:
  Renewables - Electricity Generation: Renewable electricity displacing the use of natural gas
  Renewables - Transport: Biodiesel and bioethanol displacing the use of petrol and diesel
  Renewables - Heat: Consumption of renewable heat displacing the consumption of oil
  Biomethane: Consumption of biomethane displacing the consumption of natural gas
Energy demand data sourced from National Energy Projections produced by SEAI
Fossil fuel emission factors sourced from National GHG Inventory

## Slide 16: Non-energy PaMs
Agriculture and LULUCF policies and measures are isolated in the GHG projections by the sectoral expert
e.g. the planned measure ‘Extended forestry rotation’ is linked to the LULUCF accounting category ‘Managed forest land’
  Difference between WEM and WAM GHG projection for this category captures a bigger source of emissions under WEM moving to a smaller source under WAM (the effect of extended forestry rotation)

## Slide 17
SEAI energy savings
EPA Emission Factors
PaMs Tool
Data Processing
[MS Excel]
Annex (PaMs attributes and progress)
Extract, Transform, Load
(Mostly manual)
Load
Annex XIV
(Air Quality)
Integrated national policies and measures – GovReg
Transform
(Manual)
Other energy and non-energy PaMs
[e.g. Ag, LULUCF, Renewables]

## Slide 18: Unique PaM IDs
Reporting field requires that each PaM has a unique ID
  Ensures consistency across reporting cycles
  Useful for lookup formulas to pull data from data processing files to import template

## Slide 19: PaMs Improvement process
Continuing to develop and expand work on PaMs
Annual QA/QC feedback from the ETC-CM acts as a starting point
Ongoing improvements include:
  Enhancing alignment with national GHG projections
  methodology updates for in-house calculations
  improving ex-post analysis of PaMs
  updating qualitative information behind each PaM (e.g., descriptions, assumptions, links to Union dimensions and policies)
  process documentation

## Slide 20
The national system for PaMs and Projections

## Slide 21: Institutional arrangements
Ireland’s Environmental Protection Agency (EPA) designated as the national entity with overall responsibility for reporting on policies and measures (PaMs) and GHG projections
The Minister for Climate, Energy and the Environment has overall responsibility for climate change policy and coordination of the development of the national policies and measures in climate change mitigation and adaptation
The EPA works with the following organisations to clearly understand the assumptions, methodologies and models underpinning projections and PaMs associated with relevant sectors:
  Sustainable Energy Authority of Ireland (SEAI)
  Economic and Social Research Institute (ESRI)
  Teagasc (The Irish Agriculture and Food Development Authority)
  Government Departments

## Slide 22: Stakeholder engagement
Engagement process is well established
Main stakeholders consulted in the preparation of GHG emission projections and Policies and Measures are:
  Sustainable Energy Authority of Ireland (SEAI)
  Economic and Social Research Institute (ESRI), with input from Department of Finance
  Government Departments (Climate, Energy and the Environment , Enterprise Trade and Employment, Housing Local Government and Heritage, Transport)
  Teagasc (The Irish Agriculture and Food Development Authority) and Department of Agriculture, Food and the Marine

## Slide 23: Alignment with national inventory system
National system for PaMs and projections builds on the National Atmospheric Inventory System (NAIS) for Ireland which was established by Government Decision in 2007
The EPA has developed and implemented practices in the development of greenhouse gas emission projections which broadly follow the processes and arrangements in place for the national inventory system:
  Incorporation of the projections data processing into the national emission inventory file structures
  Development of QA/QC procedures like those in place for national emission inventories
  Extending the remit of national emission inventory system Memoranda of Understanding with key data providers to include the supply of activity data for national greenhouse gas and air pollutant emission projections